CODE: Generalized Öpik-type collision probability for eccentric coplanar target
by Petr Pokorný

This code is based on the article Pokorný, Petr; Vokrouhlický, David (2013),Icarus, Volume 226, Issue 1, p. 682-693 (henceforth PV2013). The main purpose of the code is to evaluate the collisional probability of a projectile (asteroid, comet, dust particle) with a target which is assumed to be on a coplanar and eccentric orbit. The code does not calculate the probability of collisions over a short timescales (hundreds of years). Since it is based on assumption of random distribution of the longitudes of the ascending node W it gives correct estimates over longer timescales when the W of target and projectile move effectively through all possible relative orientations. The code thus cannot be used for the estimating the short and medium-term collisional risks to the Earth. However, as we proved in PV2013 the code works pretty well on long timescales.

Inputs: Subroutine WETKOZ require several input variables to properly evaluate the collisional probability
Orbital elements of the projectile (e.g. NEO)
- Semimajor-axis of the projectile - in astronomical units (au = 149,597,870,700 m)
- Eccentricity of the projectile - that should be 0 < e < 1
- Inclination of the projectile - in radians.
- Argument of pericenter of the projectile – in radians
Orbital elements of the target (e.g. Earth)
- Semimajor-axis of the target- in astronomical units (au = 149,597,870,700 m)
- Eccentricity of the target - that should be 0 < e < 1

Outputs: Default output from the WETKOZ subroutine is the intrinsic collision probability in units ( au-2 yr-1 ) (EQ. 29 in PV2013). Let us calculate the collisional probability of 4179 Toutatis with the Earth-like target without a knowledge of its crosssection:
a4179 = 2.5294 au
e4179 = 0.62943
i4179 = 0.44602°
w4179 = 278.55°

aEarth = 1.0 au
eEarth = 0.01671123

Collisional probability = 11.13768 – output form the subroutine WETKOZ

Thus if you want to evaluate e.g. the collisional probability of a 4179 Toutatis with the Earth per year, just multiply the intrinsic collisional probability by square of the radius of the Earth ( Rearth = 6371 km = 4.2588 x 10-5 ) - the factor p is already included in the code, thus we use only r2 instead of p.r2 and we get a result 1.995 x 10-8 for Toutatis.

Additional Outputs:
During the evaluation of the collisional probability the code also evaluates many additional variables, that may be useful for various tasks. For each impact configuration (up to 8 impact configurations for each heliocentric distance of the target) the code evaluates values eccentricity, inclination and argument of pericenter when the impact configuration can occur. In such points the code also evaluates relative velocity vector of the target and projectile and also radiants as seen from the target.

How to run it:
The code is written in F90 standard so you can use your favorite Fortran compiler to compile it, e.g. gfortran CODE.f90 -o CODE -O3, where -O3 is the optimization flag so it runs faster. Then in Linux you run it simply by ./CODE < IN where the IN file contains all required inputs. See the source code that is fairly commented and in case of any questions don’t hesitate to contact me at petr.pokorny@nasa.gov.